## Slide 1: Three Parts of the Scoreboard
Instruction status—which of 4 steps the instruction is in
Functional unit status—Indicates the state of the functional unit (FU). 9 fields for each functional unit
  Busy—Indicates whether the unit is busy or not
  Op—Operation to perform in the unit (e.g., + or –)
  Fi—Destination register
  Fj, Fk—Source-register numbers
  Qj, Qk—Functional units producing source registers Fj, Fk
  Rj, Rk—Flags indicating when Fj, Fk are ready
Register result status—Indicates which functional unit will write each register, if one exists. Blank when no pending instructions will write that register

## Slide 2: Detailed Scoreboard Pipeline Control

## Slide 3: Detailed Scoreboard Pipeline Control
Stage | Wait until... (The Condition to Proceed) | Bookkeeping (What the Scoreboard Does)
1. Issue | 1. The required Functional Unit (FU) is free. 2. The destination register is not already waiting for a result from another instruction. | 1. Mark the Functional Unit as Busy. 2. Mark the destination register as "waiting for this FU's result." 3. Check if source registers (S1, S2) are ready: • If a source is ready, set its Ready flag to Yes. • If a source is not ready, note which FU it's waiting for and set Ready to No.
2. Read operands | Both source operands for the instruction have their Ready flags set to Yes. (This resolves RAW / Read-After-Write hazards, ensuring data is available before use.) | 1. Set the Ready flags for this instruction back to No (since the operands have now been read).
3. Execution complete | The Functional Unit has finished its calculation (e.g., the addition or multiplication is done). | (No bookkeeping actions. The result is just held in the FU, waiting to be written.)
4. Write result | No other instruction (which was issued earlier) is still waiting to read the old value from this instruction's destination register. (This resolves WAR / Write-After-Read hazards, preventing an old instruction from reading a new value prematurely.) | 1. Notify all waiting instructions: Tell any other instructions that were waiting for this result that their operand is now Ready (set their flags to Yes). 2. Free the destination register: Clear its status so other instructions can write to it. 3. Free the Functional Unit: Mark the FU as No longer Busy.

## Slide 4: Scoreboard Example
Instruction Status |  |  | 
Instruction |  | j | k
LD | F6 | 34+ | R2
LD | F2 | 45+ | R3
MULT | F0 | F2 | F4
SUBD | F8 | F6 | F2
DIVD | F10 | F0 | F6
ADDD | F6 | F8 | F2
Issue | Read Operand | Execution Completion | Write Result
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | No |  |  |  |  |  |  |  | 
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
 | FU |  |  |  |  |  |  |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 5: Scoreboard Example Cycle 1
Instruction Status |  |  | 
Instruction |  | j | k
LD | F6 | 34+ | R2
LD | F2 | 45+ | R3
MULT | F0 | F2 | F4
SUBD | F8 | F6 | F2
DIVD | F10 | F0 | F6
ADDD | F6 | F8 | F2
Issue | Read Operand | Execution Completion | Write Result
1 |  |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | Yes | Load | F6 |  | R2 |  |  |  | Yes
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | No |  |  |  |  |  |  |  | 
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
1 | FU |  |  |  | Integer |  |  |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 6: Scoreboard Example Cycle 2
Instruction Status |  |  | 
Instruction |  | j | k
LD | F6 | 34+ | R2
LD | F2 | 45+ | R3
MULT | F0 | F2 | F4
SUBD | F8 | F6 | F2
DIVD | F10 | F0 | F6
ADDD | F6 | F8 | F2
Issue | Read Operand | Execution Completion | Write Result
1 | 2 |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | Yes | Load | F6 |  | R2 |  |  |  | Yes
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | No |  |  |  |  |  |  |  | 
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
2 | FU |  |  |  | Integer |  |  |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 7: Scoreboard Example Cycle 3
Instruction Status |  |  | 
Instruction |  | j | k
LD | F6 | 34+ | R2
LD | F2 | 45+ | R3
MULT | F0 | F2 | F4
SUBD | F8 | F6 | F2
DIVD | F10 | F0 | F6
ADDD | F6 | F8 | F2
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 3 | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | Yes | Load | F6 |  | R2 |  |  |  | Yes
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | No |  |  |  |  |  |  |  | 
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
3 | FU |  |  |  | Integer |  |  |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 8: Scoreboard Example Cycle 4
Instruction Status |  |  | 
Instruction |  | j | k
LD | F6 | 34+ | R2
LD | F2 | 45+ | R3
MULT | F0 | F2 | F4
SUBD | F8 | F6 | F2
DIVD | F10 | F0 | F6
ADDD | F6 | F8 | F2
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 3 | 4
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | Yes | Load | F6 |  | R2 |  |  |  | Yes
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | No |  |  |  |  |  |  |  | 
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
4 | FU |  |  |  | Integer |  |  |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 9: Scoreboard Example Cycle 5
Instruction Status |  |  | 
Instruction |  | j | k
LD | F6 | 34+ | R2
LD | F2 | 45+ | R3
MULT | F0 | F2 | F4
SUBD | F8 | F6 | F2
DIVD | F10 | F0 | F6
ADDD | F6 | F8 | F2
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 3 | 4
5 |  |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | Yes | Load | F2 |  | R3 |  |  |  | Yes
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | No |  |  |  |  |  |  |  | 
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
5 | FU |  | Integer |  |  |  |  |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 10: Scoreboard Example Cycle 6
Instruction Status |  |  | 
Instruction |  | j | k
LD | F6 | 34+ | R2
LD | F2 | 45+ | R3
MULT | F0 | F2 | F4
SUBD | F8 | F6 | F2
DIVD | F10 | F0 | F6
ADDD | F6 | F8 | F2
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 3 | 4
5 | 6 |  | 
6 |  |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | Yes | Load | F2 |  | R3 |  |  |  | Yes
 | Mult 1 | Yes | Mult | F0 | F2 | F4 | Integer |  | No | Yes
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | No |  |  |  |  |  |  |  | 
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
6 | FU | Mult 1 | Integer |  |  |  |  |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 11: Scoreboard Example Cycle 7
Instruction Status |  |  | 
Instruction |  | j | k
LD | F6 | 34+ | R2
LD | F2 | 45+ | R3
MULT | F0 | F2 | F4
SUBD | F8 | F6 | F2
DIVD | F10 | F0 | F6
ADDD | F6 | F8 | F2
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 3 | 4
5 | 6 | 7 | 
6 |  |  | 
7 |  |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | Yes | Load | F2 |  | R3 |  |  |  | Yes
 | Mult 1 | Yes | Mult | F0 | F2 | F4 | Integer |  | No | Yes
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | Sub | F8 | F6 | F2 |  | Integer | Yes | No
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
7 | FU | Mult 1 | Integer |  |  | Add |  |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 12: Scoreboard Example Cycle 8a
Instruction Status |  |  | 
Instruction |  | j | k
LD | F6 | 34+ | R2
LD | F2 | 45+ | R3
MULT | F0 | F2 | F4
SUBD | F8 | F6 | F2
DIVD | F10 | F0 | F6
ADDD | F6 | F8 | F2
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 3 | 4
5 | 6 | 7 | 
6 |  |  | 
7 |  |  | 
8 |  |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | Yes | Load | F2 |  | R3 |  |  |  | Yes
 | Mult 1 | Yes | Mult | F0 | F2 | F4 | Integer |  | No | Yes
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | Sub | F8 | F6 | F2 |  | Integer | Yes | No
 | Divide | Yes | Div | F10 | F0 | F6 | Mult 1 |  | No | Yes
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
8 | FU | Mult 1 | Integer |  |  | Add | Divide |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 13: Scoreboard Example Cycle 8b
Instruction Status |  |  | 
Instruction |  | j | k
LD | F6 | 34+ | R2
LD | F2 | 45+ | R3
MULT | F0 | F2 | F4
SUBD | F8 | F6 | F2
DIVD | F10 | F0 | F6
ADDD | F6 | F8 | F2
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 3 | 4
5 | 6 | 7 | 8
6 |  |  | 
7 |  |  | 
8 |  |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
 | Mult 1 | Yes | Mult | F0 | F2 | F4 |  |  | Yes | Yes
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | Sub | F8 | F6 | F2 |  |  | Yes | Yes
 | Divide | Yes | Div | F10 | F0 | F6 | Mult 1 |  | No | Yes
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
8 | FU | Mult 1 |  |  |  | Add | Divide |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 14: Scoreboard Example Cycle 9
Instruction Status |  |  | 
Instruction |  | j | k
LD | F6 | 34+ | R2
LD | F2 | 45+ | R3
MULT | F0 | F2 | F4
SUBD | F8 | F6 | F2
DIVD | F10 | F0 | F6
ADDD | F6 | F8 | F2
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 3 | 4
5 | 6 | 7 | 8
6 | 9 |  | 
7 | 9 |  | 
8 |  |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
10 | Mult 1 | Yes | Mult | F0 | F2 | F4 |  |  | Yes | Yes
 | Mult 2 | No |  |  |  |  |  |  |  | 
2 | Add | Yes | Sub | F8 | F6 | F2 |  |  | Yes | Yes
 | Divide | Yes | Div | F10 | F0 | F6 | Mult 1 |  | No | Yes
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
9 | FU | Mult 1 |  |  |  | Add | Divide |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 15: Scoreboard Example Cycle 11
Instruction Status |  |  | 
Instruction |  | j | k
LD | F6 | 34+ | R2
LD | F2 | 45+ | R3
MULT | F0 | F2 | F4
SUBD | F8 | F6 | F2
DIVD | F10 | F0 | F6
ADDD | F6 | F8 | F2
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 3 | 4
5 | 6 | 7 | 8
6 | 9 |  | 
7 | 9 | 11 | 
8 |  |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
8 | Mult 1 | Yes | Mult | F0 | F2 | F4 |  |  | Yes | Yes
 | Mult 2 | No |  |  |  |  |  |  |  | 
0 | Add | Yes | Sub | F8 | F6 | F2 |  |  | Yes | Yes
 | Divide | Yes | Div | F10 | F0 | F6 | Mult 1 |  | No | Yes
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
11 | FU | Mult 1 |  |  |  | Add | Divide |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 16: Scoreboard Example Cycle 12
Instruction Status |  |  | 
Instruction |  | j | k
LD | F6 | 34+ | R2
LD | F2 | 45+ | R3
MULT | F0 | F2 | F4
SUBD | F8 | F6 | F2
DIVD | F10 | F0 | F6
ADDD | F6 | F8 | F2
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 3 | 4
5 | 6 | 7 | 8
6 | 9 |  | 
7 | 9 | 11 | 12
8 |  |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
7 | Mult 1 | Yes | Mult | F0 | F2 | F4 |  |  | Yes | Yes
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | No |  |  |  |  |  |  |  | 
 | Divide | Yes | Div | F10 | F0 | F6 | Mult 1 |  | No | Yes
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
12 | FU | Mult 1 |  |  |  |  | Divide |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 17: Scoreboard Example Cycle 13
Instruction Status |  |  | 
Instruction |  | j | k
LD | F6 | 34+ | R2
LD | F2 | 45+ | R3
MULT | F0 | F2 | F4
SUBD | F8 | F6 | F2
DIVD | F10 | F0 | F6
ADDD | F6 | F8 | F2
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 3 | 4
5 | 6 | 7 | 8
6 | 9 |  | 
7 | 9 | 11 | 12
8 |  |  | 
13 |  |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
6 | Mult 1 | Yes | Mult | F0 | F2 | F4 |  |  | Yes | Yes
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | Add | F6 | F8 | F2 |  |  | Yes | Yes
 | Divide | Yes | Div | F10 | F0 | F6 | Mult 1 |  | No | Yes
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
13 | FU | Mult 1 |  |  | Add |  | Divide |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 18: Scoreboard Example Cycle 14
Instruction Status |  |  | 
Instruction |  | j | k
LD | F6 | 34+ | R2
LD | F2 | 45+ | R3
MULT | F0 | F2 | F4
SUBD | F8 | F6 | F2
DIVD | F10 | F0 | F6
ADDD | F6 | F8 | F2
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 3 | 4
5 | 6 | 7 | 8
6 | 9 |  | 
7 | 9 | 11 | 12
8 |  |  | 
13 | 14 |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
5 | Mult 1 | Yes | Mult | F0 | F2 | F4 |  |  | Yes | Yes
 | Mult 2 | No |  |  |  |  |  |  |  | 
2 | Add | Yes | Add | F6 | F8 | F2 |  |  | Yes | Yes
 | Divide | Yes | Div | F10 | F0 | F6 | Mult 1 |  | No | Yes
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
14 | FU | Mult 1 |  |  | Add |  | Divide |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 19: Scoreboard Example Cycle 15
Instruction Status |  |  | 
Instruction |  | j | k
LD | F6 | 34+ | R2
LD | F2 | 45+ | R3
MULT | F0 | F2 | F4
SUBD | F8 | F6 | F2
DIVD | F10 | F0 | F6
ADDD | F6 | F8 | F2
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 3 | 4
5 | 6 | 7 | 8
6 | 9 |  | 
7 | 9 | 11 | 12
8 |  |  | 
13 | 14 |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
4 | Mult 1 | Yes | Mult | F0 | F2 | F4 |  |  | Yes | Yes
 | Mult 2 | No |  |  |  |  |  |  |  | 
1 | Add | Yes | Add | F6 | F8 | F2 |  |  | Yes | Yes
 | Divide | Yes | Div | F10 | F0 | F6 | Mult 1 |  | No | Yes
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
15 | FU | Mult 1 |  |  | Add |  | Divide |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 20: Scoreboard Example Cycle 16
Instruction Status |  |  | 
Instruction |  | j | k
LD | F6 | 34+ | R2
LD | F2 | 45+ | R3
MULT | F0 | F2 | F4
SUBD | F8 | F6 | F2
DIVD | F10 | F0 | F6
ADDD | F6 | F8 | F2
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 3 | 4
5 | 6 | 7 | 8
6 | 9 |  | 
7 | 9 | 11 | 12
8 |  |  | 
13 | 14 | 16 | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
3 | Mult 1 | Yes | Mult | F0 | F2 | F4 |  |  | Yes | Yes
 | Mult 2 | No |  |  |  |  |  |  |  | 
0 | Add | Yes | Add | F6 | F8 | F2 |  |  | Yes | Yes
 | Divide | Yes | Div | F10 | F0 | F6 | Mult 1 |  | No | Yes
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
16 | FU | Mult 1 |  |  | Add |  | Divide |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 21: Scoreboard Example Cycle 17
Instruction Status |  |  | 
Instruction |  | j | k
LD | F6 | 34+ | R2
LD | F2 | 45+ | R3
MULT | F0 | F2 | F4
SUBD | F8 | F6 | F2
DIVD | F10 | F0 | F6
ADDD | F6 | F8 | F2
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 3 | 4
5 | 6 | 7 | 8
6 | 9 |  | 
7 | 9 | 11 | 12
8 |  |  | 
13 | 14 | 16 | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
2 | Mult 1 | Yes | Mult | F0 | F2 | F4 |  |  | Yes | Yes
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | Add | F6 | F8 | F2 |  |  | Yes | Yes
 | Divide | Yes | Div | F10 | F0 | F6 | Mult 1 |  | No | Yes
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
17 | FU | Mult 1 |  |  | Add |  | Divide |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 22: Scoreboard Example Cycle 18
Instruction Status |  |  | 
Instruction |  | j | k
LD | F6 | 34+ | R2
LD | F2 | 45+ | R3
MULT | F0 | F2 | F4
SUBD | F8 | F6 | F2
DIVD | F10 | F0 | F6
ADDD | F6 | F8 | F2
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 3 | 4
5 | 6 | 7 | 8
6 | 9 |  | 
7 | 9 | 11 | 12
8 |  |  | 
13 | 14 | 16 | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
1 | Mult 1 | Yes | Mult | F0 | F2 | F4 |  |  | Yes | Yes
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | Add | F6 | F8 | F2 |  |  | Yes | Yes
 | Divide | Yes | Div | F10 | F0 | F6 | Mult 1 |  | No | Yes
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
18 | FU | Mult 1 |  |  | Add |  | Divide |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 23: Scoreboard Example Cycle 19
Instruction Status |  |  | 
Instruction |  | j | k
LD | F6 | 34+ | R2
LD | F2 | 45+ | R3
MULT | F0 | F2 | F4
SUBD | F8 | F6 | F2
DIVD | F10 | F0 | F6
ADDD | F6 | F8 | F2
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 3 | 4
5 | 6 | 7 | 8
6 | 9 | 19 | 
7 | 9 | 11 | 12
8 |  |  | 
13 | 14 | 16 | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
0 | Mult 1 | Yes | Mult | F0 | F2 | F4 |  |  | Yes | Yes
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | Add | F6 | F8 | F2 |  |  | Yes | Yes
 | Divide | Yes | Div | F10 | F0 | F6 | Mult 1 |  | No | Yes
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
19 | FU | Mult 1 |  |  | Add |  | Divide |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 24: Scoreboard Example Cycle 20
Instruction Status |  |  | 
Instruction |  | j | k
LD | F6 | 34+ | R2
LD | F2 | 45+ | R3
MULT | F0 | F2 | F4
SUBD | F8 | F6 | F2
DIVD | F10 | F0 | F6
ADDD | F6 | F8 | F2
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 3 | 4
5 | 6 | 7 | 8
6 | 9 | 19 | 20
7 | 9 | 11 | 12
8 |  |  | 
13 | 14 | 16 | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | Add | F6 | F8 | F2 |  |  | Yes | Yes
 | Divide | Yes | Div | F10 | F0 | F6 |  |  | Yes | Yes
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
20 |  |  |  |  | Add |  | Divide |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 25: Scoreboard Example Cycle 21
Instruction Status |  |  | 
Instruction |  | j | k
LD | F6 | 34+ | R2
LD | F2 | 45+ | R3
MULT | F0 | F2 | F4
SUBD | F8 | F6 | F2
DIVD | F10 | F0 | F6
ADDD | F6 | F8 | F2
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 3 | 4
5 | 6 | 7 | 8
6 | 9 | 19 | 20
7 | 9 | 11 | 12
8 | 21 |  | 
13 | 14 | 16 | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | Add | F6 | F8 | F2 |  |  | Yes | Yes
 | Divide | Yes | Div | F10 | F0 | F6 |  |  | Yes | Yes
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
21 |  |  |  |  | Add |  | Divide |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 26: Scoreboard Example Cycle 22
Instruction Status |  |  | 
Instruction |  | j | k
LD | F6 | 34+ | R2
LD | F2 | 45+ | R3
MULT | F0 | F2 | F4
SUBD | F8 | F6 | F2
DIVD | F10 | F0 | F6
ADDD | F6 | F8 | F2
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 3 | 4
5 | 6 | 7 | 8
6 | 9 | 19 | 20
7 | 9 | 11 | 12
8 | 21 |  | 
13 | 14 | 16 | 22
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | No |  |  |  |  |  |  |  | 
40 | Divide | Yes | Div | F10 | F0 | F6 |  |  | Yes | Yes
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
22 |  |  |  |  |  |  | Divide |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 27: Scoreboard Example Cycle 61
Instruction Status |  |  | 
Instruction |  | j | k
LD | F6 | 34+ | R2
LD | F2 | 45+ | R3
MULT | F0 | F2 | F4
SUBD | F8 | F6 | F2
DIVD | F10 | F0 | F6
ADDD | F6 | F8 | F2
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 3 | 4
5 | 6 | 7 | 8
6 | 9 | 19 | 20
7 | 9 | 11 | 12
8 | 21 | 61 | 
13 | 14 | 16 | 22
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | No |  |  |  |  |  |  |  | 
0 | Divide | Yes | Div | F10 | F0 | F6 |  |  | Yes | Yes
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
61 |  |  |  |  |  |  | Divide |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 28: Scoreboard Example Cycle 62
Instruction Status |  |  | 
Instruction |  | j | k
LD | F6 | 34+ | R2
LD | F2 | 45+ | R3
MULT | F0 | F2 | F4
SUBD | F8 | F6 | F2
DIVD | F10 | F0 | F6
ADDD | F6 | F8 | F2
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 3 | 4
5 | 6 | 7 | 8
6 | 9 | 19 | 20
7 | 9 | 11 | 12
8 | 21 | 61 | 62
13 | 14 | 16 | 22
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | No |  |  |  |  |  |  |  | 
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
62 |  |  |  |  |  |  |  |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles