## Slide 1: Three Parts of the Scoreboard
Instruction status—which of 4 steps the instruction is in
Functional unit status—Indicates the state of the functional unit (FU). 9 fields for each functional unit
  Busy—Indicates whether the unit is busy or not
  Op—Operation to perform in the unit (e.g., + or –)
  Fi—Destination register
  Fj, Fk—Source-register numbers
  Qj, Qk—Functional units producing source registers Fj, Fk
  Rj, Rk—Flags indicating when Fj, Fk are ready
Register result status—Indicates which functional unit will write each register, if one exists. Blank when no pending instructions will write that register

## Slide 2: Detailed Scoreboard Pipeline Control

## Slide 3: Detailed Scoreboard Pipeline Control
Stage | Wait until... (The Condition to Proceed) | Bookkeeping (What the Scoreboard Does)
1. Issue | 1. The required Functional Unit (FU) is free. 2. The destination register is not already waiting for a result from another instruction. | 1. Mark the Functional Unit as Busy. 2. Mark the destination register as "waiting for this FU's result." 3. Check if source registers (S1, S2) are ready: • If a source is ready, set its Ready flag to Yes. • If a source is not ready, note which FU it's waiting for and set Ready to No.
2. Read operands | Both source operands for the instruction have their Ready flags set to Yes. (This resolves RAW / Read-After-Write hazards, ensuring data is available before use.) | 1. Set the Ready flags for this instruction back to No (since the operands have now been read).
3. Execution complete | The Functional Unit has finished its calculation (e.g., the addition or multiplication is done). | (No bookkeeping actions. The result is just held in the FU, waiting to be written.)
4. Write result | No other instruction (which was issued earlier) is still waiting to read the old value from this instruction's destination register. (This resolves WAR / Write-After-Read hazards, preventing an old instruction from reading a new value prematurely.) | 1. Notify all waiting instructions: Tell any other instructions that were waiting for this result that their operand is now Ready (set their flags to Yes). 2. Free the destination register: Clear its status so other instructions can write to it. 3. Free the Functional Unit: Mark the FU as No longer Busy.

## Slide 4: Scoreboard Example 2
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | No |  |  |  |  |  |  |  | 
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
 | FU |  |  |  |  |  |  |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 5: Scoreboard Example 2 - Cycle 1
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 |  |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | No |  |  |  |  |  |  |  | 
 | Divide | Yes | DIVD | F0 | F2 | F4 |  |  | Yes | Yes
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
1 | FU | Divide |  |  |  |  |  |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 6: Scoreboard Example 2 – Cycle 2
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 |  | 
2 |  |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | Yes | LD | F6 |  | R1 |  |  |  | Yes
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | No |  |  |  |  |  |  |  | 
 | Divide | Yes | DIVD | F0 | F2 | F4 |  |  | Yes | Yes
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
2 | FU | Divide |  |  | Integer |  |  |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 7: Scoreboard Example 2 – Cycle 3
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 |  | 
2 | 3 |  | 
3 |  |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | Yes | LD | F6 |  | R1 |  |  |  | Yes
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | ADDD | F10 | F0 | F8 | Divide |  | No | Yes
40 | Divide | Yes | DIVD | F0 | F2 | F4 |  |  | Yes | Yes
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
3 | FU | Divide |  |  | Integer |  | Add |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 8: Scoreboard Example 2 – Cycle 4
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 |  | 
2 | 3 | 4 | 
3 |  |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | Yes | LD | F6 |  | R1 |  |  |  | Yes
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | ADDD | F10 | F0 | F8 | Divide |  | No | Yes
39 | Divide | Yes | DIVD | F0 | F2 | F4 |  |  | Yes | Yes
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
4 | FU | Divide |  |  | Integer |  | Add |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 9: Scoreboard Example 2 – Cycle 5
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 |  | 
2 | 3 | 4 | 5
3 |  |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | ADDD | F10 | F0 | F8 | Divide |  | No | Yes
38 | Divide | Yes | DIVD | F0 | F2 | F4 |  |  | Yes | Yes
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
5 | FU | Divide |  |  |  |  | Add |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 10: Scoreboard Example 2 – Cycle 6
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 |  | 
2 | 3 | 4 | 5
3 |  |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | ADDD | F10 | F0 | F8 | Divide |  | No | Yes
37 | Divide | Yes | DIVD | F0 | F2 | F4 |  |  | Yes | Yes
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
6 | FU | Divide |  |  |  |  | Add |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 11: Scoreboard Example 2 – Cycle 42
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 42 | 
2 | 3 | 4 | 5
3 |  |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | ADDD | F10 | F0 | F8 | Divide |  | No | Yes
0 | Divide | Yes | DIVD | F0 | F2 | F4 |  |  | Yes | Yes
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
42 | FU | Divide |  |  |  |  | Add |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 12: Scoreboard Example 2 – Cycle 43
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 42 | 43
2 | 3 | 4 | 5
3 |  |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | ADDD | F10 | F0 | F8 | Divide |  | Yes | Yes
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
43 | FU |  |  |  |  |  | Add |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 13: Scoreboard Example 2 – Cycle 44
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 42 | 43
2 | 3 | 4 | 5
3 | 44 |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | ADDD | F10 | F0 | F8 | Divide |  | Yes | Yes
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
44 | FU |  |  |  |  |  | Add |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 14: Scoreboard Example 2 – Cycle 46
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 42 | 43
2 | 3 | 4 | 5
3 | 44 | 46 | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | ADDD | F10 | F0 | F8 | Divide |  | Yes | Yes
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
46 | FU |  |  |  |  |  | Add |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 15: Scoreboard Example 2 – Cycle 47
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 42 | 43
2 | 3 | 4 | 5
3 | 44 | 46 | 47
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | ADDD | F10 | F0 | F8 | Divide |  | Yes | Yes
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
47 | FU |  |  |  |  |  | Add |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 16: Scoreboard Example 2 – Cycle 48
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 42 | 43
2 | 3 | 4 | 5
3 | 44 | 46 | 47
48 |  |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | SUBD | F8 | F12 | F14 |  |  | Yes | Yes
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
48 | FU |  |  |  |  | Add |  |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 17: Scoreboard Example 2 – Cycle 49
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 42 | 43
2 | 3 | 4 | 5
3 | 44 | 46 | 47
48 | 49 |  | 
49 |  |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
 | Mult 1 | Yes | MULT | F12 | F6 | F2 |  |  | Yes | Yes
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | SUBD | F8 | F12 | F14 |  |  | Yes | Yes
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
49 | FU |  |  |  |  | Add |  | Mult 1 |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 18: Scoreboard Example 2 – Cycle 50
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 42 | 43
2 | 3 | 4 | 5
3 | 44 | 46 | 47
48 | 49 |  | 
49 | 50 |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
 | Mult 1 | Yes | MULT | F12 | F6 | F2 |  |  | Yes | Yes
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | SUBD | F8 | F12 | F14 |  |  | Yes | Yes
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
50 | FU |  |  |  |  | Add |  | Mult 1 |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 19: Scoreboard Example 2 – Cycle 51
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 42 | 43
2 | 3 | 4 | 5
3 | 44 | 46 | 47
48 | 49 | 51 | 
49 | 50 |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
10 | Mult 1 | Yes | MULT | F12 | F6 | F2 |  |  | Yes | Yes
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | SUBD | F8 | F12 | F14 |  |  | Yes | Yes
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
51 | FU |  |  |  |  | Add |  | Mult 1 |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 20: Scoreboard Example 2 – Cycle 52
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 42 | 43
2 | 3 | 4 | 5
3 | 44 | 46 | 47
48 | 49 | 51 | 52
49 | 50 |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
9 | Mult 1 | Yes | MULT | F12 | F6 | F2 |  |  | Yes | Yes
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | SUBD | F8 | F12 | F14 |  |  | Yes | Yes
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
52 | FU |  |  |  |  | Add |  | Mult 1 |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 21: Scoreboard Example 2 – Cycle 53
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 42 | 43
2 | 3 | 4 | 5
3 | 44 | 46 | 47
48 | 49 | 51 | 52
49 | 50 |  | 
53 |  |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
8 | Mult 1 | Yes | MULT | F12 | F6 | F2 |  |  | Yes | Yes
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | ADDD | F10 | F12 | F14 | Mult 1 |  | No | Yes
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
53 | FU |  |  |  |  |  | Add | Mult 1 |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 22: Scoreboard Example 2 – Cycle 54
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 42 | 43
2 | 3 | 4 | 5
3 | 44 | 46 | 47
48 | 49 | 51 | 52
49 | 50 |  | 
53 |  |  | 
54 |  |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | Yes | LD | F8 |  | R1 |  |  |  | Yes
7 | Mult 1 | Yes | MULT | F12 | F6 | F2 |  |  | Yes | Yes
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | ADDD | F10 | F12 | F14 | Mult 1 |  | No | Yes
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
54 | FU |  |  |  |  | Integer | Add | Mult 1 |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 23: Scoreboard Example 2 – Cycle 55
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 42 | 43
2 | 3 | 4 | 5
3 | 44 | 46 | 47
48 | 49 | 51 | 52
49 | 50 |  | 
53 |  |  | 
54 | 55 |  | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | Yes | LD | F8 |  | R1 |  |  |  | Yes
6 | Mult 1 | Yes | MULT | F12 | F6 | F2 |  |  | Yes | Yes
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | ADDD | F10 | F12 | F14 | Mult 1 |  | No | Yes
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
55 | FU |  |  |  |  | Integer | Add | Mult 1 |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 24: Scoreboard Example 2 – Cycle 56
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 42 | 43
2 | 3 | 4 | 5
3 | 44 | 46 | 47
48 | 49 | 51 | 52
49 | 50 |  | 
53 |  |  | 
54 | 55 | 56 | 
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | Yes | LD | F8 |  | R1 |  |  |  | Yes
5 | Mult 1 | Yes | MULT | F12 | F6 | F2 |  |  | Yes | Yes
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | ADDD | F10 | F12 | F14 | Mult 1 |  | No | Yes
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
56 | FU |  |  |  |  | Integer | Add | Mult 1 |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 25: Scoreboard Example 2 – Cycle 57
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 42 | 43
2 | 3 | 4 | 5
3 | 44 | 46 | 47
48 | 49 | 51 | 52
49 | 50 |  | 
53 |  |  | 
54 | 55 | 56 | 57
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | Yes | LD | F8 |  | R1 |  |  |  | Yes
4 | Mult 1 | Yes | MULT | F12 | F6 | F2 |  |  | Yes | Yes
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | ADDD | F10 | F12 | F14 | Mult 1 |  | No | Yes
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
57 | FU |  |  |  |  | Integer | Add | Mult 1 |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 26: Scoreboard Example 2 – Cycle 58
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 42 | 43
2 | 3 | 4 | 5
3 | 44 | 46 | 47
48 | 49 | 51 | 52
49 | 50 |  | 
53 |  |  | 
54 | 55 | 56 | 57
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
3 | Mult 1 | Yes | MULT | F12 | F6 | F2 |  |  | Yes | Yes
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | ADDD | F10 | F12 | F14 | Mult 1 |  | No | Yes
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
58 | FU |  |  |  |  |  | Add | Mult 1 |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 27: Scoreboard Example 2 – Cycle 60
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 42 | 43
2 | 3 | 4 | 5
3 | 44 | 46 | 47
48 | 49 | 51 | 52
49 | 50 | 60 | 
53 |  |  | 
54 | 55 | 56 | 57
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
0 | Mult 1 | Yes | MULT | F12 | F6 | F2 |  |  | Yes | Yes
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | ADDD | F10 | F12 | F14 | Mult 1 |  | No | Yes
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
60 | FU |  |  |  |  |  | Add | Mult 1 |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 28: Scoreboard Example 2 – Cycle 61
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 42 | 43
2 | 3 | 4 | 5
3 | 44 | 46 | 47
48 | 49 | 51 | 52
49 | 50 | 60 | 61
53 |  |  | 
54 | 55 | 56 | 57
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
 | Mult 1 | Yes | MULT | F12 | F6 | F2 |  |  | Yes | Yes
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | ADDD | F10 | F12 | F14 | Mult 1 |  | Yes | Yes
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
61 | FU |  |  |  |  |  | Add | Mult 1 |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 29: Scoreboard Example 2 – Cycle 62
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 42 | 43
2 | 3 | 4 | 5
3 | 44 | 46 | 47
48 | 49 | 51 | 52
49 | 50 | 60 | 61
53 | 62 |  | 
54 | 55 | 56 | 57
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | ADDD | F10 | F12 | F14 | Mult 1 |  | Yes | Yes
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
62 | FU |  |  |  |  |  | Add |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 30: Scoreboard Example 2 – Cycle 64
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 42 | 43
2 | 3 | 4 | 5
3 | 44 | 46 | 47
48 | 49 | 51 | 52
49 | 50 | 60 | 61
53 | 62 | 64 | 
54 | 55 | 56 | 57
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | ADDD | F10 | F12 | F14 | Mult 1 |  | Yes | Yes
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
64 | FU |  |  |  |  |  | Add |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 31: Scoreboard Example 2 – Cycle 65
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 42 | 43
2 | 3 | 4 | 5
3 | 44 | 46 | 47
48 | 49 | 51 | 52
49 | 50 | 60 | 61
53 | 62 | 64 | 65
54 | 55 | 56 | 57
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | Yes | ADDD | F10 | F12 | F14 | Mult 1 |  | Yes | Yes
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
65 | FU |  |  |  |  |  | Add |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles

## Slide 32: Scoreboard Example 2 – Cycle 66
Instruction Status |  |  | 
Instruction |  | j | k
DIVD | F0 | F2 | F4
LD | F6 | 0+ | R1
ADDD | F10 | F0 | F8
SUBD | F8 | F12 | F14
MULT | F12 | F6 | F2
ADDD | F10 | F12 | F14
LD | F8 | 8+ | R1
Issue | Read Operand | Execution Completion | Write Result
1 | 2 | 42 | 43
2 | 3 | 4 | 5
3 | 44 | 46 | 47
48 | 49 | 51 | 52
49 | 50 | 60 | 61
53 | 62 | 64 | 65
54 | 55 | 56 | 57
Functional Unit Status |  | Busy | Op | dest Fi | S1 Fj | S2 Fk | FU for Qj | FU for Qk | Fj? Rj | Fk? Rk
Time | Name |  |  |  |  |  |  |  |  | 
 | Integer | No |  |  |  |  |  |  |  | 
 | Mult 1 | No |  |  |  |  |  |  |  | 
 | Mult 2 | No |  |  |  |  |  |  |  | 
 | Add | No |  |  |  |  |  |  |  | 
 | Divide | No |  |  |  |  |  |  |  | 
Register Result Status |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ….. | F30
Clock |  |  |  |  |  |  |  |  |  | 
66 | FU |  |  |  |  |  |  |  |  | 
Integer Unit | 1 cycle
FP Adder Unit | 2 cycles
FP Multiplier | 10 cycles
FP Divider | 40 cycles